## Slide 1: Swift short term optimizer
Modeling & Implementation

## Slide 2: The Problem
A short term optimizer that can optimize the daily generation for a given period (one month up to a year)
A tool for both planner / schedulers
Inputs
  Daily Price Forecast
  Initial Elevation
  Daily Inflow Forecast
  Forebay Targets (Optional)
  Daily Generation Targets (Optional)
  Operating constraints (Optional)
A perfect opportunity to study quadratic optimization
  A much ‘cleaner’ model than the Slice one

## Slide 3: The Hydro model
Vol = 0.0078Fb2 - 10.986Fb + 3958.3 (Natalie) [388.9,772.3]
Fb = 704.23078 + 11.32277 * sqrt(vol - 89.96) [900-1000]
Hk = 14.36 + 0.907 * sqrt(Vol – 89.96) [30-38]
Gen = Hk * TurbFlow
Disch = TurbFlow + Spill
Vol[i+1] = Vol[i] + Inflow[i] – Disch[i]

## Slide 4: The Optimization Objective
The total revenue
  \sum_i (Prices[i] * Qp[i] * Hk[i]), i = 1,…,n
    Non-linear!
Total penalty for deviating from the Forebay (or Volume) Targets
    \sum_i (vol_target_penalty[i] * | Vol[i] – Vol_Target[i] |)
Total penalty for deviating from the Generation Targets
      \sum_i (gen_target_penalty[i] * | Gen[i] – Gen_Target[i] |)
      Non-Linear!
Water value function (Optional)
  We value the remaining water in the reservoir by the average price in the optimization period

## Slide 5: Modeling Challenge
Not possible to implement the quadratic objective directly
    \sum_i (Prices[i] * Qp[i] * Hk[i]), i = 1,…,n
Note PSD = Convexity!
  Cholesky decomposition: Q is PSD, iff exists H, s.t. Q = HTH
  So, for any x, xTQx = xTHTHx = |Hx|2 >= 0 (PSD)
Absolute values are hard to model if it contains non-linear term
      \sum_i (gen_target_penalty[i] * | Gen[i] – Gen_Target*[i] |)

## Slide 6: Trick - Separation of Variables
x * y = u2 – v2 where u = (x+y)/2, v = (x-y)/2
So
    Σ(Prices[i] * Qp[i] * Hk[i]) Σ(Prices[i] * (u[i] 2+ v[i] 2))
Then use piecewise linear (PWL) objective for u2 and v2, respectively.
PWL: a new feature added in Gurobi 6.5!
Gurobi converts them to SOS2 Constraints
  At most two are non-negative
  Non-negative ones must be adjacent

## Slide 7: Same trick continues…
How to deal with absolute values?
  Turn them into quadratic terms instead
  Similarly:
    (xy-c) 2 = x2y2 – 2xy + c2
    Note that x2y2 = ((x+y)4 + (x-y)4 – (2x4 + 2y4))/12
    So x2y2 = (u4 + v4) * 4 / 3 – (x4 + y4) / 6, u = (x+y)/2, v = (x-y)/2
  So far, all the multiplicative terms are separated!
  However, we end up with much more complex models (with lots of SOS2 constraints)
      Σ(gen_target_penalty[i] * | Gen[i] – Gen_Target*[i] |)

## Slide 8: Implementation
Python 2.7
Gurobi 6.5
qo[i] = m.addVar(lb=minQo, ub=maxQo, name='qo_{i}'.format(i = i))
m.addConstr(qo[i] == qp[i] + qs[i],'disch_{i}'.format(i=i))
m.setPWLObj(u[i], ucoords, prices[i] * np.power(ucoords, 2))
schedules['Revenue'] = [g * p for (g,p) in zip(schedules['Generation'], prices)]
Variable
X coordinates
Y coordinates

## Slide 9: Optimize to Prices
Optimize to random daily prices
Optimizer purposely maintains a high forebay to get high H/Ks
<10 secs to optimize a three-month model

## Slide 10: Optimize to Targets
Initial Forebay = 936
Two Fb Targets: 925 and 935
Random Generation Targets
2-5 minutes to find a decent solution for an 3-month model with daily gen targets
Trying to hit the forebay target for the second half of the month

## Slide 11: Future Work
How to combine with Natalie’s long term stochastic model?
Any simpler approach to model generation targets?
Can Slice Optimizer benefit from this work?
  Content function is not linear or quadratic
    Can still model using PWL and SOS2 constraints
    Performance can be an issue
Any other PUD with dispatch-able hydro project?

## Slide 12: Comments/Questions?